## Slide 1: Chapter 2: Application Layer
Yanmin Zhu
School of Computers

## Slide 2
Discussions
What is the Application Layer about?
As a developer, what knowledge do you lack?
How do you architect a distributed application?
What services does a network application require from the lower layer?

## Slide 3: Chapter 2: Our goals
conceptual, implementation aspects of network application protocols
  transport-layer service models
  client-server paradigm
  peer-to-peer paradigm
learn about protocols by examining popular application-level protocols
  HTTP
  FTP
  SMTP / POP3 / IMAP
  DNS
programming network applications
  socket API

## Slide 4: Some network apps
e-mail
web
instant messaging
remote login
P2P file sharing
multi-user network games
streaming stored video clips
social networks
voice over IP
real-time video conferencing
cloud computing
video games

## Slide 5: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 6: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 7: Creating a network appication
write programs that
  run on (different) end systems
  communicate over network
  e.g., web server software communicates with browser software
No need to write software for network-core devices
  Network-core devices do not run user applications
  applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 8: Application architectures
Client-server
  Including data centers / cloud computing
Peer-to-peer (P2P)
Hybrid of client-server and P2P

## Slide 9: Client-server architecture
server:
  always-on host
  permanent IP address
  server farms for scaling
clients:
  communicate with server
  may be intermittently connected
  may have dynamic IP addresses
  do not communicate directly with each other
client/server

## Slide 10: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
Highly scalable but difficult to manage
peer-peer

## Slide 11: Hybrid of client-server and P2P
Skype
  voice-over-IP P2P application
  centralized server: finding address of remote party:
  client-client connection: direct (not through server)
Instant messaging
  chatting between two users is P2P
  centralized service: client presence detection/location
    user registers its IP address with central server when it comes online
    user contacts central server to find IP addresses of buddies

## Slide 12: Processes communicating
Process: program running within a host.
within same host, two processes communicate using inter-process communication (defined by OS, e.g., pipe).
processes in different hosts communicate by exchanging messages
Client process: process that initiates communication
Server process: process that waits to be contacted
Note: applications with P2P architectures have client processes & server processes

## Slide 13: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door which brings message to socket at receiving process
process
TCP with
buffers,
variables
socket
host or
server
process
TCP with
buffers,
variables
socket
host or
server
Internet
controlled
by OS
controlled by
app developer
API: (1) choice of transport protocol; (2) ability to fix a few parameters
Notes: Shove 挤出 shAf

## Slide 14: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Exercise: use ipconfig from command prompt to get your IP address (Windows)
Q: does IP address of host on which process runs suffice for identifying the process?
  A: No, many processes can be running on same
Identifier includes both IP address and port numbers associated with process on host.
Example port numbers:
  HTTP server: 80
  Mail server: 25

## Slide 15: App-layer protocol defines
Message syntax:
  what fields in messages & how fields are delineated
Message semantics
  meaning of information in fields
Types of messages exchanged,
  e.g., request, response
Rules for when and how processes send & respond to messages
Public-domain protocols:
  defined in RFCs
  allows for interoperability
  e.g., HTTP, SMTP, BitTorrent
Proprietary protocols:
  e.g., Skype, ppstream

## Slide 16: What transport service need?
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, telnet) require 100% reliable data transfer
Throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
Security
Encryption, data integrity, …

## Slide 17: Fun

## Slide 18: Transport service requirements
Application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
instant messaging
Data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
Throughput
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
Time Sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 19: Internet transport protocols services
TCP service:
  connection-oriented: setup required between client and server processes
  reliable transport between sending and receiving process
  flow control: sender won’t overwhelm receiver
  congestion control: throttle sender when network overloaded
  does not provide: timing, minimum throughput guarantees, security
UDP service:
  unreliable data transfer between sending and receiving process
  does not provide: connection setup, reliability, flow control, congestion control, timing, throughput guarantee, or security
Q: why bother? Why is there a UDP?
Notes: ['θrɒt(ə)l]

## Slide 20: Internet apps vs. transport protocols
Application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
Application
layer protocol
SMTP [RFC 2821]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (eg Youtube), RTP [RFC 1889]
SIP, RTP, proprietary
(e.g., Skype)
Underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
typically UDP

## Slide 21: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 22
Discussions
What are typical HTTP messages?
HTTP is stateless, how to develop a shopping web application over HTTP?
Why is HTTP widely used for Web apps?

## Slide 23: WWW: A Milestone of the Internet!
Before WWW was invented in 1990, what did people do with the Internet?

## Slide 24: Overview
Web Server
Apache HTTP Server
IBM HTTP Server
Google Chrome
Microsoft Edge
Mozilla Firefox
Safari

## Slide 25: Web and HTTP
First some jargon
  Web page consists of objects
  Object can be HTML file, JPEG image, Java applet, audio file,…
  Web page consists of base HTML-file which includes several referenced objects
Each object is addressable by a URL
  Example URL:
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 26: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, “displays” Web objects
  server: Web server sends objects in response to requests
PC running
Explorer
Server
running
Apache Web
server
Mac running
Navigator
HTTP request
HTTP request
HTTP response
HTTP response

## Slide 27: HTTP overview (continued)
Uses TCP:
  client initiates TCP connection (creates socket) to server, port 80
  server accepts TCP connection from client
  HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
  TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
Protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside
Notes: ['rek(ə)nsaɪl]
vt. 使一致；使和解；调停，调解；使顺从

## Slide 28: HTTP connections
Non-persistent HTTP
At most one object is sent over a TCP connection.
Persistent HTTP
Multiple objects can be sent over single TCP connection between client and server.

## Slide 29: Nonpersistent HTTP
Suppose user enters URL www.someSchool.edu/someDepartment/home.index
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text,
references to 10
jpeg images)

## Slide 30: Nonpersistent HTTP (cont.)
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 31: Non-Persistent HTTP: Response time
Definition of RTT: time for a small packet to travel from client to server and back.
Response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
total = 2RTT+transmit time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 32: Persistent HTTP
Issues of Nonpersistent HTTP
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects
Persistent HTTP
  server leaves connection open after sending response
  subsequent HTTP messages between same client/server sent over open connection
  client sends requests as soon as it encounters a referenced object
  as little as one RTT for all the referenced objects

## Slide 33: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language:fr
(extra carriage return, line feed)
request line
(GET, POST,
HEAD commands)
header
lines
Carriage return,
line feed
indicates end
of message

## Slide 34: HTTP request message: general format

## Slide 35: Uploading form input
Post method:
Uses POST method
Input is uploaded to server in entity body
URL method:
Uses GET method
Input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana
Web page often includes form input

## Slide 36: Method types
HTTP/1.0
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 37: HTTP response message
HTTP/1.1 200 OK
Connection close
Date: Thu, 06 Aug 1998 12:00:15 GMT
Server: Apache/1.3.0 (Unix)
Last-Modified: Mon, 22 Jun 1998 …...
Content-Length: 6821
Content-Type: text/html
data data data data data ...
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file

## Slide 38: HTTP response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (Location:)
400 Bad Request
  request message not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
In first line in server->client response message. A few sample codes:

## Slide 39: Trying out HTTP (client side)
1. Telnet to your favorite Web server:
Opens TCP connection to port 80
(default HTTP server port) at cis.poly.edu.
Anything typed in sent
to port 80 at www.sjtu.edu.cn
telnet www.sjtu.edu.cn 80
2. Type in a GET HTTP request:
GET / HTTP/1.1
Host: www.sjtu.edu.cn
By typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. Look at response message sent by the HTTP server!
Notes: Ssh www.cs.sjtu.edu.cn
telnet www.cs.sjtu.edu.cn
GET /~yzhu/index.html HTTP/1.1
Host: www.cs.sjtu.edu.cn

## Slide 40: HTTP/2
Key goal: decreased delay in multi-object HTTP requests
HTTP1.1: introduced multiple, pipelined GETs over single TCP connection
server responds in-order (FCFS: first-come-first-served scheduling) to GET requests
with FCFS, small object may have to wait for transmission (head-of-line (HOL) blocking) behind large object(s)
loss recovery (retransmitting lost TCP segments) stalls object transmission
Notes: t’

## Slide 41: HTTP/2
HTTP/2: [RFC 7540, 2015] increased flexibility at server in sending objects to client:
methods, status codes, most header fields unchanged from HTTP 1.1
transmission order of requested objects based on client-specified object priority (not necessarily FCFS)
push unrequested objects to client
divide objects into frames, schedule frames to mitigate HOL blocking
Key goal: decreased delay in multi-object HTTP requests
Notes: t’

## Slide 42: HTTP/2: mitigating HOL blocking
HTTP 1.1: client requests 1 large object (e.g., video file) and 3 smaller objects
client
server
GET O1
GET O2
GET O3
GET O4
O1
O2
O3
O4
object data requested
O1
O2
O3
O4
objects delivered in order requested: O2, O3, O4 wait behind O1
Notes: t’

## Slide 43: HTTP/2: mitigating HOL blocking
HTTP/2: objects divided into frames, frame transmission interleaved
client
server
GET O1
GET O2
GET O3
GET O4
O2
O4
object data requested
O1
O2
O3
O4
O2, O3, O4 delivered quickly, O1 slightly delayed
O3
O1
Notes: shortest job first: decreased average delay!

## Slide 44: HTTP/2 to HTTP/3
HTTP/2 over single TCP connection means:
  recovery from packet loss still stalls all object transmissions
  no security over vanilla TCP connection
HTTP/3: adds security, per object error- and congestion-control (more pipelining) over UDP
Notes: t’

## Slide 45: QUIC: Quick UDP Internet Connections
application-layer protocol, on top of UDP
  increase performance of HTTP
  deployed on many Google servers, apps (Chrome, mobile YouTube app)
IP
TCP
TLS
HTTP/2
IP
UDP
QUIC
HTTP/2 (slimmed)
Network
Transport
Application
HTTP/2 over TCP
HTTP/3
HTTP/2 over QUIC over UDP

## Slide 46: QUIC: Quick UDP Internet Connections
adopts approaches we’ll study in chapter for connection establishment, error control, congestion control
  error and congestion control: “Readers familiar with TCP’s loss detection and congestion control will find algorithms here that parallel well-known TCP ones.” [from QUIC specification]
  connection establishment: reliability, congestion control, authentication, encryption, state established in one RTT

## Slide 47: QUIC: Connection establishment
TCP handshake
(transport layer)
TLS handshake
(security)
TCP (reliability, congestion control state) + TLS (authentication, crypto state)
2 serial handshakes
data
data
QUIC: reliability, congestion control, authentication, crypto state
1 handshake
QUIC
1RTT handshake

## Slide 48: QUIC: 0-RTT Connection establishment
data
TLS session ticket sent by server, cached at client
end of first QUIC connection
start of second QUIC connection
Client uses last session ticket for encryption, authentication for new connection
0 RTT handshake delay
data

## Slide 49: What a RFC look like?
1 Introduction.............................................7
2 Notational Conventions and Generic Grammar..............13
3 Protocol Parameters.....................................17
4 HTTP Message............................................30
5 Request.................................................34
6 Response................................................38
7 Entity..................................................41
8 Connections.............................................43
9 Method Definitions......................................48
10 Status Code Definitions................................53
11 Access Authentication..................................65
12 Content Negotiation....................................67
13 Caching in HTTP........................................70
14 Header Field Definitions...............................94
15 Security Considerations...............................139
16 Acknowledgments.......................................144
17 References............................................146
18 Authors' Addresses....................................149
19 Appendices............................................150

## Slide 50: RFC 1945: HTTP/1.0

## Slide 51: RFC 2068: HTTP/1.1

## Slide 52: RFC 7540 HTTP/2
Notes: HTTP/2 is a major revision of the HTTP network protocol, used by the World Wide Web. It was developed by the Internet Engineering Task Force (IETF) and published in 2015. Here are some key features of HTTP/2:
Binary Protocol: Unlike HTTP/1.1, which is text-based, HTTP/2 is binary. This makes it more efficient to parse and less error-prone.
Multiplexing: Multiple requests and responses can be sent simultaneously over a single TCP connection, reducing latency and improving page load times.
Header Compression: HTTP/2 uses HPACK compression to reduce the overhead of HTTP headers, which can be significant in HTTP/1.1.
Server Push: Servers can send resources to the client before they are requested, potentially speeding up page loads.
Stream Prioritization: Clients can assign priority levels to different streams, allowing more important resources to be delivered first.
Overall, HTTP/2 improves performance, efficiency, and speed compared to HTTP/1.1, especially in modern web applications.

## Slide 53: RFC 9114 HTTP/3

## Slide 54
Shall we maintain the states of a web client?
Why and how?

## Slide 55: User-server state: cookies
Many major Web sites use cookies
Four components:
  1) cookie header line of HTTP response message
  2) cookie header line in HTTP request message
  3) cookie file kept on user’s host, managed by user’s browser
  4) back-end database at Web site
Example:
Susan always access Internet always from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID

## Slide 56: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
Set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie-
spectific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 57: Cookies (continued)
What cookies can bring:
authorization
shopping carts
recommendations
user session state (Web e-mail)
Cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
How to keep “state”:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: http messages carry state

## Slide 58: Web caches (proxy server)
user sets browser: Web accesses via proxy
browser sends all HTTP requests to proxy
  if object in cache: cache returns object
  else proxy requests object from origin server, then returns object to client
Goal: satisfy client request without involving origin server
client
Proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 59: More about Web caching
proxy acts as both client and server
typically proxy is installed by ISP (university, company, residential ISP)
Why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link.
Internet dense with proxy : enables “poor” content providers to effectively deliver content (but so does P2P file sharing)

## Slide 60: Caching example
Assumptions
average object size = 1,000,000 bits
avg. request rate from institution’s browsers to origin servers = 15/sec
delay from institutional router to any origin server and back to router = 2 sec
Consequences
utilization on LAN = 15%
utilization on access link = 100%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + milliseconds
origin
servers
public
Internet
institutional
network
100 Mbps LAN
15 Mbps
access link
institutional
cache

## Slide 61: Caching example (cont)
possible solution
increase bandwidth of access link to, say, 100 Mbps
consequence
utilization on LAN = 15%
utilization on access link = 15%
Total delay = Internet delay + access delay + LAN delay
= 2 sec + msecs + msecs
often a costly upgrade
origin
servers
public
Internet
institutional
network
100 Mbps LAN
100 Mbps
access link
institutional
cache

## Slide 62: Caching example (cont)
possible solution: install cache
suppose hit rate is 0.4
consequence
40% requests will be satisfied almost immediately
60% requests satisfied by origin server
utilization of access link reduced to 60%, resulting in negligible delays (say 10 msec)
total avg delay = Internet delay + access delay + LAN delay = .6*(2.01) secs + .4*milliseconds < 1.4 secs
origin
servers
public
Internet
institutional
network
100 Mbps LAN
15 Mbps
access link
institutional
cache
Any problem with Web caching?

## Slide 63: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
proxy : specify date of cached copy in HTTP request
  If-modified-since: <date>
server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
proxy
server
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified

## Slide 64
Already having HTTP, why should we make another protocol for file transfer?
What are typical FTP messages?

## Slide 65: FTP: the file transfer protocol
transfer file to/from remote host
client/server model
  client: side that initiates transfer (either to/from remote)
  server: remote host
file transfer
FTP
server
FTP
user
interface
FTP
client
local file
system
remote file
system
user
at host
ftp: RFC 959
ftp server: port 21

## Slide 66: FTP: separate control, data connections
FTP client contacts FTP server at port 21, TCP is transport protocol
client authorized over control connection
client browses remote directory by sending commands over control connection.
when server receives file transfer command, server opens 2nd TCP connection (for file) to client
after transferring one file, server closes data connection.
FTP
client
FTP
server
TCP control connection
port 21
TCP data connection
port 20
server opens another TCP data connection to transfer another file.
control connection: “out of band”
FTP server maintains “state”: current directory, earlier authentication

## Slide 67: FTP commands, responses
Sample commands:
sent as ASCII text over control channel
USER username
PASS password
LIST return list of file in current directory
RETR filename retrieves (gets) file
STOR filename stores (puts) file onto remote host
Sample return codes
status code and phrase (as in HTTP)
331 Username OK, password required
125 data connection already open; transfer starting
425 Can’t open data connection
452 Error writing file

## Slide 68: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 69
Compared with web and file transfer, what’s unique for emails?
Notes: 用户账号
发出去后，对方不一定马上在线接收

## Slide 70: Overview: Electronic Mail
Three major components:
  user agents
  mail servers
  simple mail transfer protocol: SMTP
  User Agent
    a.k.a. “mail reader”
    composing, editing, reading mail messages
    e.g.,Outlook, Firefox, elm, Mozilla Thunderbird
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP

## Slide 71: Electronic Mail: mail servers
Mail Servers
  mailbox contains incoming messages for user
  message queue of outgoing (to be sent) mail messages
SMTP protocol [RFC 2821]
between mail servers to send email messages
  client: sending mail to server
  “server”: receiving mail server
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP

## Slide 72: Electronic Mail: SMTP
uses TCP to reliably transfer email message from client to server, port 25
direct transfer: sending server to receiving server
three phases of transfer
  1) handshaking (greeting)
  2) transfer of messages
  3) closure
command/response interaction
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCII

## Slide 73: Scenario: Alice sends message to Bob
1) Alice uses UA to compose message and “to” bob@someschool.edu
2) Alice’s UA sends message to her mail server; message placed in message queue
3) Client side of SMTP opens TCP connection with Bob’s mail server
4) SMTP client sends Alice’s message over the TCP connection
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message
user
agent
mail
server
mail
server
user
agent
1
2
3
4
5
6
SMTP
SMTP
SMTP
How to get the address of bob’s mail server?

## Slide 74: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection
Notes: telnet mail.cs.sjtu.edu 25
HELO cs.sjtu.edu.cn
MAIL FROM: www.cs.sjtu.edu.cn
RCPT TO: <yzhu@sjtu.edu.cn>
DATA
Success on march 6, 2016

## Slide 75: Try SMTP interaction for yourself:
telnet servername 25
see 220 reply from server
enter HELO, MAIL FROM, RCPT TO, DATA, QUIT commands
above lets you send email without using email client (reader)

## Slide 76: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
Comparison with HTTP:
HTTP: pull
SMTP: push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response msg
SMTP: multiple objects sent in multipart msg

## Slide 77: Mail message format
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:
header lines, e.g.,
  To:
  From:
  Subject:
  different from SMTP commands!
body
  the “message”, ASCII characters only
header
body
blank
line

## Slide 78: Mail access protocols
SMTP: delivery/storage to receiver’s server
Mail access protocol: retrieval from server
  1) POP: Post Office Protocol [RFC 1939]
    authorization (agent <-->server) and download
  2) IMAP: Internet Mail Access Protocol [RFC 1730]
    more features (more complex)
    manipulation of stored msgs on server
  3) HTTP: gmail, Hotmail, Yahoo! Mail, etc.
user
agent
sender’s mail
server
user
agent
SMTP
SMTP
access
protocol
receiver’s mail
server

## Slide 79: POP3 protocol
authorization phase
client commands:
  user: declare username
  pass: password
server responses
  +OK
  -ERR
transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
C: list
S: 1 498
S: 2 912
S: .
C: retr 1
S: <message 1 contents>
S: .
C: dele 1
C: retr 2
S: <message 1 contents>
S: .
C: dele 2
C: quit
S: +OK POP3 server signing off
S: +OK POP3 server ready
C: user bob
S: +OK
C: pass hungry
S: +OK user successfully logged on
Notes: telnet mail.cs.sjtu.edu.cn 80
user yzhu
pass ???
list
retr ??

## Slide 80: POP3 (more) and IMAP
More about POP3
Previous example uses “download and delete” mode.
Bob cannot re-read e-mail if he changes client
“Download-and-keep”: copies of messages on different clients
POP3 is stateless across sessions
IMAP
Keep all messages in one place: the server
Allows user to organize messages in folders
IMAP keeps user state across sessions:
  names of folders and mappings between message IDs and folder name

## Slide 81: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 82: DNS: Domain Name System
People: many identifiers:
  ID, passport #
  names
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., ww.yahoo.com - used by humans
Q: how do we map between IP addresses and names?

## Slide 83
Is it always necessary to translate names to IPs?
Do you have an approach to mapping names to IP addresses?

## Slide 84: Domain Name System:
distributed database
  implemented in hierarchy of many name servers
application-layer protocol
  host, routers, name servers to communicate to resolve names (address/name translation)
note: core Internet function, but implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 85: DNS
DNS services
hostname to IP address translation
host aliasing
  Canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: set of IP addresses for one canonical name
Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
doesn’t scale!

## Slide 86: Distributed, Hierarchical Database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
Client wants IP for www.amazon.com;
client queries a root server to find com DNS server
client queries com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com

## Slide 87: DNS: Root name servers
contacted by local name server that can not resolve name
root name server:
  contacts authoritative name server if name mapping not known
  gets mapping
  returns mapping to local name server
13 root name servers worldwide
b USC-ISI Marina del Rey, CA
l ICANN Los Angeles, CA
e NASA Mt View, CA
f Internet Software C. Palo Alto, CA (and 36 other locations)
i Autonomica, Stockholm (plus 28 other locations)
k RIPE London (also 16 other locations)
m WIDE Tokyo (also Seoul, Paris, SF)
a Verisign, Dulles, VA
c Cogent, Herndon, VA (also LA)
d U Maryland College Park, MD
g US DoD Vienna, VA
h ARL Aberdeen, MD
j Verisign, ( 21 locations)

## Slide 88: TLD and Authoritative Servers
Top-level domain (TLD) servers:
  responsible for com, org, net, edu, etc, and all top-level country domains uk, fr, ca, jp.
  Network Solutions maintains servers for com TLD
  Education for edu TLD
Authoritative DNS servers:
  organization’s DNS servers, providing authoritative hostname to IP mappings for organization’s servers (e.g., Web, mail).
  can be maintained by organization or service provider

## Slide 89: Local Name Server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one.
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  acts as proxy, forwards query into hierarchy

## Slide 90: Example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”
Notes: 迭代的

## Slide 91: Example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
3
recursive query:
puts burden of name resolution on contacted name server
heavy load?

## Slide 92: DNS: caching and updating records
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time
  TLD servers typically cached in local name servers
    Thus root name servers not often visited
update/notify mechanisms under design by IETF
  RFC 2136
  http://www.ietf.org/html.charters/dnsind-charter.html

## Slide 93: DNS records
DNS: distributed db storing resource records (RR)
Type=NS
  name is domain (e.g. foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
Type=A
  name is hostname
  value is IP address
Type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really
  servereast.backup2.ibm.com
  value is canonical name
Type=MX
  value is name of mailserver associated with name
(www.ibm.com, servereast.backup2.ibm.com)

## Slide 94: DNS protocol, messages
query and reply messages, both with same message format
message header
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes

## Slide 95: DNS protocol, messages
name, type fields
for a query
RRs in response
to query
records for
authoritative servers
additional “helpful”
info that may be used
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes

## Slide 96
You start a new company (www.ali99.com) (web + mail)
What are the records inserted in to the hierarchy?

## Slide 97: Inserting records into DNS
requesting host
www.ali99.com
root DNS server
local DNS server
authoritative DNS server
dns.ali99.com
.com top-level DNS server
www.ali99.com
mail.ali99.com

## Slide 98: Inserting records into DNS
register name ali99.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into com TLD server:
  (ali99.com, dns.ali99.com, NS)
  (dns.ali99.com, 212.212.212.1, A)
create authoritative server
  Type A record for www. ali99.com: (www.ali99.com, 212.212.212.100, A)
  Type MX record for ali99.com: (ali99.com, 212.212.212.101, MX)

## Slide 99: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 100: Pure P2P architecture
no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses
Applications:
  File distribution
  Video streaming
peer-peer

## Slide 101
What are the advantages of P2P over C/S?

## Slide 102: File Distribution: Server-Client vs P2P
Question : How much time to distribute file from one server to N peers?
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
File, size F
us: server upload bandwidth
ui: peer i upload bandwidth
di: peer i download bandwidth

## Slide 103: File distribution time: server-client
server sequentially sends N copies:
  NF/us time
client i takes F/di time to download
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
F
increases linearly in N
(for large N)
= dcs = max { NF/us, F/min(di) }
i
Time to distribute F
to N clients using
client/server approach

## Slide 104: File distribution time: P2P
server must send one copy: F/us time
client i takes F/di time to download
NF bits must be downloaded (aggregate)
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
F
fastest possible upload rate: us + Sui
dP2P = max { F/us, F/min(di) , NF/(us + Sui) }
i

## Slide 105: Server-client vs. P2P: example
Client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us

## Slide 106: File distribution: BitTorrent
tracker: tracks peers
participating in torrent
torrent: group of
peers exchanging
chunks of a file
obtain list
of peers
trading
chunks
peer
Bram Cohen
Published on April, 2001

## Slide 107: Torrent File
A .torrent file is a text file, which consists of two parts
(1) Information about Tracker
(2) Information about the file to be shared
  index of the blocks of the file
  hash value of each block

## Slide 108: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Web Server
.torrent

## Slide 109: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Web Server

## Slide 110: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Response-peer list
Web Server

## Slide 111: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Shake-hand
Web Server
Shake-hand

## Slide 112: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
Web Server

## Slide 113: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
pieces
pieces
pieces
Web Server

## Slide 114: Overall Architecture
Web page
with link
to .torrent
A
B
C
Peer
[Leech]
Downloader
“US”
Peer
[Seed]
Peer
[Leech]
Tracker
Get-announce
Response-peer list
pieces
pieces
pieces
Web Server

## Slide 115: BitTorrent (1)
file divided into 256KB chunks.
peer joining torrent:
  has no chunks, but will accumulate them over time
  registers with tracker to get list of peers, connects to subset of peers (“neighbors”)
while downloading, peer uploads chunks to other peers.
peers may come and go
once peer has entire file, it may (selfishly) leave or (altruistically) remain

## Slide 116: BitTorrent (2)
Sending Chunks: tit-for-tat
Alice sends chunks to four neighbors currently sending her chunks at the highest rate
  re-evaluate top 4 every 10 secs
every 30 secs: randomly select another peer, starts sending chunks
  newly chosen peer may join top 4
Pulling Chunks
at any given time, different peers have different subsets of file chunks
periodically, a peer (Alice) asks each neighbor for list of chunks that they have.
Alice sends requests for her missing chunks
  rarest first

## Slide 117
How do we organize peers and files in a distributed way? Users can search and download files from the p2p network

## Slide 118: A Straightforward Solution
Forrest Gump
Query
Forrest Gump
A
B
C
D
F
G
H
I
J

## Slide 119
Better solutions?

## Slide 120: Basic Idea
A
B
C
D
f1
f1
f2
f3
f3
f3
f2
f2
f4
A structure
organizing both peers and index
index
f1
f2
f3
f4
A
C
A
B
D
D
(key, value)
A
B
C
D
A
B
D
Where to get f1?

## Slide 121: Simple Database for Storing Index
Key (File name) | Value (IP Address)
The Zookeeper's Wife | 202.120.2.1
Ghost in the Shell | 202.120.1.8, 202.120.100.3
……. | 
……. | 
Forrest Gump | 202.112.3.4
The Index, i.e., (key, value) pairs!

## Slide 122: Hash Table
More convenient to store and search on numerical representation of key
Original Key (File name) | Numerical Key | Value (IP Address)
The Zookeeper's Wife | 02 | 202.120.2.1
Ghost in the Shell | 05 | 202.120.1.8, 202.120.100.3
……. |  | 
……. |  | 
Forrest Gump | 02 | 202.112.3.4
key = hash(original key)
The Index, i.e., (key, value) pairs !

## Slide 123: Distributed Hash Table (DHT)
Distribute (key, value) pairs over millions of peers
  pairs are evenly distributed over peers
Any peer can query DHT with a key
  DHT returns the value for the key
Each peer only knows about a small number of other peers
A
B
C
D
(key, value)
(key, value)
(key, value)
(key, value)

## Slide 124
How do you distribute (key, value) pairs over peers?
What are objectives?
A
B
C
D
(key, value)
(key, value)
(key, value)
(key, value)
Notes: Continuous playout -> end-to-end throughput
High bandwidth requirements on servers

## Slide 125: Chord: Basic Idea
Original Key (File name) | Key IDs | Value (IP Address)
The Zookeeper's Wife | 2 | 202.120.5.18
Ghost in the Shellz | 5 | 202.120.1.8, 202.120.100.3
……. |  | 
……. |  | 
Forrest Gump | 2 | 202.112.3.4
Key-Value Pairs
Peer IP | Peer ID
202.120.2.1 | 2
202.120.1.8 | 3
……. | 
202.120.100.3 | 5
……. | 
Peers
Key hashed to ID space
IP hashed to ID space
Assignment
(The Zookeeper’s wife, 202.120.5.18)
(Forrest Gump, 202.112.3.4)
(Ghost in the Shellz, 202.120.1.8/202.120.100.3 )

## Slide 126: Chord: details
rule: assign key-value pair to the peer that has the closest ID.
convention: closest is the immediate successor of the key.
e.g., ID space {0,1,2,3,…,63}
suppose 8 peers: 1,12,13,25,32,40,48,60
  If key = 51, then assigned to peer 60
  If key = 60, then assigned to peer 60
  If key = 61, then assigned to peer 1

## Slide 127: Circular DHT
1
12
13
25
32
40
48
60
“overlay network”

## Slide 128: Resolving a query
1
12
13
25
32
40
48
60
What is the value (IP) associated with key 53 ?
value
O(N) messages
on average to resolve
query, when there
are N peers

## Slide 129: Circular DHT with shortcuts
each peer keeps track of IP addresses of predecessor, successor, short cuts.
reduced from 6 to 3 messages.
possible to design shortcuts with O(log N) neighbors, O(log N) messages in query
1
12
13
25
32
40
48
60
What is the value (IP) for
key 53
value

## Slide 130: Peer churn
example: peer 5 abruptly leaves
1
3
4
5
8
10
12
15
handling peer churn:
peers may come and go (churn)
each peer knows address of its two successors
each peer periodically pings its two successors to check aliveness
if immediate successor leaves, choose next successor as new immediate successor

## Slide 131: Peer churn
example: peer 5 abruptly leaves
peer 4 detects peer 5’s departure; makes 8 its immediate successor
4 asks 8 who its immediate successor is; makes 8’s immediate successor its second successor.
1
3
4
8
10
12
15
handling peer churn:
peers may come and go (churn)
each peer knows address of its two successors
each peer periodically pings its two successors to check aliveness
if immediate successor leaves, choose next successor as new immediate successor

## Slide 132: Roadmap
2.1 Principles of network applications
2.2 Web and HTTP
2.3 FTP
2.4 Electronic Mail
2.5 DNS
2.5 P2P applications
2.6 Video Streaming and CDN

## Slide 133
What are unique characteristics of video streaming applications?
Notes: Continuous playout -> end-to-end throughput
High bandwidth requirements on servers

## Slide 134: Video Streaming and CDNs: context
video traffic: major consumer of Internet bandwidth
  Netflix, YouTube: 37%, 16% of downstream residential ISP traffic
  ~1B YouTube users, ~75M Netflix users
Challenge 1: heterogeneity
  different users have different capabilities (e.g., wired versus mobile; bandwidth rich versus bandwidth poor)
Challenge 2: scale - how to reach ~1B users?
  single mega-video server won’t work (why?)

## Slide 135: Multimedia: video
video: sequence of images displayed at constant rate
  e.g., 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 136: Video encoding
Coding examples:
MPEG 1 (CD-ROM) 1.5 Mbps
MPEG2 (DVD) 3-6 Mbps
MPEG4 (often used in Internet, < 1 Mbps)
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 137: Streaming stored video:
simple scenario:
video server
(stored video)
client
Internet

## Slide 138
Challenge 1: heterogeneity
How do we address it?

## Slide 139: Streaming multimedia: DASH
server:
  divides video file into multiple chunks
  each chunk stored, encoded at different rates
  manifest file: provides URLs for different chunks
client:
  periodically measures server-to-client bandwidth
  consulting manifest, requests one chunk at a time
    chooses maximum coding rate sustainable given current bandwidth
    can choose different coding rates at different points in time (depending on available bandwidth at time)
DASH: Dynamic, Adaptive Streaming over HTTP

## Slide 140: Streaming multimedia: DASH
when to request chunk (so that buffer starvation, or overflow does not occur)
what encoding rate to request (higher quality when more bandwidth available)
where to request chunk (can request from URL server that is “close” to client or has high available bandwidth)
“intelligence” at client: client determines

## Slide 141
Challenge 2: Streaming to hundreds of thousands of simultaneous users
How do we address it?

## Slide 142: Option 1: Mega-server
Disadvantages
  single point of failure
  point of network congestion
  long path to distant clients
  multiple copies of video sent over outgoing link
this solution doesn’t scale

## Slide 143: Option 2: CDN Overview
…
…
…
…
…
…
where’s Madmen?
manifest file
Content Distribution Networks
Video website
CDN server
CDN server
CDN server
CDN server
Notes: 143
Akamai: 100,000+ servers in 1000+ clusters in 1000+ networks in 70+ countries serving trillions of requests a day.
How many people use Netflix?

## Slide 144: CDN content access: a closer look
DNS redirects a user’s request to a CDN server
CDN Server IP

## Slide 145: Return which CDN server to the user?
The main idea
Step 1: the CDN learns the IP address of the user
How?
Step 2: Assign the CDN server that is geographically closest to the user host.
How?
How do we assign the CDN server that provides best performance to the user

## Slide 146: Chapter 2: Summary
typical request/reply message exchange:
  client requests info or service
  server responds with data, status code
message formats:
  headers: fields giving info about data
  data: info being communicated
Important themes:
  control vs. data msgs
    in-band, out-of-band
  centralized vs. decentralized
  stateless vs. stateful
  reliable vs. unreliable msg transfer
  “complexity at network edge”

## Slide 147: Homeworks
Chapter 01 problems:
  P1, P9, P14, P16, P25
Chapter 02 problems:
  P7, P14, P19, P27, P30
No submission required!

## Slide 148: Lab #2
One application layer protocol
  DNS (PDF)