## Slide 1: Chapter 5: Network Layer – Control Plane
Yanmin Zhu
School of Computers

## Slide 2
Discussions
What is the goal of a routing algorithm?
Is there a routing algorithm for the entire Internet?
How is the forwarding entry for a destination set up?
What is the main idea of implementing SDN?

## Slide 3: Chapter 5: chapter goals
understand principles behind network control plane
  traditional routing algorithms
  SDN controllers
  Internet Control Message Protocol (ICMP)
  network management
their instantiation, implementation in the Internet:
  OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP

## Slide 4: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 5: Network-layer functions
forwarding: move packets from router's input to appropriate router output
data plane
control plane
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination

## Slide 6: Two approaches for control plane
Approach 1: per-router control (traditional)
Approach 2: logically centralized control (software defined networking)

## Slide 7: Approach 1: Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 8: Approach 2: Logically central control plane
data
plane
control
plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 9: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 10: Goal of routing protocols
To determine “good” paths from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: one of the top networking challenges!

## Slide 11
How do you find the best path in a network?

## Slide 12: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 13: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x') = cost of link (x,x')
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 14: Routing algorithm classification
Q: global or decentralized information?
global: all routers have complete topology, link cost info
  link state algorithms
decentralized: router knows physically-connected neighbors, link costs to neighbors
  iterative process of computation, exchange of info with neighbors
  distance vector algorithms
Q: static or dynamic?
static:
  routes change slowly over time
dynamic:
  routes change more quickly
  periodic update
  in response to link cost changes

## Slide 15: Link-State: Big Picture
Each node measures cost to every neighbor
Each node sends table of neighbors to all nodes
Every node computes routing path
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 16: A link-state routing algorithm
Dijkstra's algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node ('source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.'s
notations
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 17: Dijsktra's algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 18: Dijkstra's algorithm: example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 19: Dijkstra's algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 20: Dijkstra's algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 21
Link-State is global.
Can a routing algorithm run in a fully distributed fashion, resulting in shortest path?

## Slide 22: Distance Vector: Core Idea
Bellman-Ford Equation
dx(y) = min {c(x,v) + dv(y) }
v
where min is taken over all neighbors v of x
x
y
A
B
C
2
3
5
1
7
10

## Slide 23: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node that achieves minimum is next
hop in shortest path ➜ forwarding table
B-F equation says:

## Slide 24: Distance Vector: Big Picture
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
dest | cost | next hop
v | 2 | v
x | 1 | x
w | inf | -
y | inf | -
z | inf | -
dest | cost | next hop
V |  | 
x |  | 
w |  | 
y |  | 
z |  | 
dest | cost | next hop
v |  | 
x |  | 
w |  | 
y |  | 
z |  | 
dest | cost | next hop
u | 2 | U
x | 2 | X
w | 3 | W
y | Inf | -
z | Inf | -
v’s
x’s
w’s
u’s distance vector

## Slide 25: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
Node x knows cost to each neighbor v: c(x,v)
Node x maintains distance vector Dx = [Dx(y): y є N ]
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 26: Basic Idea: Distance vector
From time-to-time, each node sends its own distance vector estimate to neighbors
Asynchronous
When a node x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converges to the actual least cost dx(y)

## Slide 27: Distance Vector Algorithm
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
Each node:

## Slide 28
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2

## Slide 29
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3

## Slide 30: Count-to-infinity problem
Count-to-infinity problem
Good news travel fast
A new neighbor A is connected to B
A neighbor A is disconnected from B
Consider all nodes’ distances to A
Notes: 交换的路径信息量大, 路径信息不一致, 收敛速度慢（坏消息）, 不适合大型网络
Distance vector routing works in theory but has a serious drawback in practice: although it converges to the correct answer, it may do so slowly. In particular, it reacts rapidly to good news, but leisurely to bad news.好消息传播得快，坏消息传播得慢, 无穷计算问题
Suddenly A goes down, or alternatively, the line between A and B is cut, which is effectively the same thing from B's point of view.
At the first packet exchange, B does not hear anything from A. Fortunately, C says: Do not worry; I have a path to A of length 2. Little does B know that C's path runs through B itself. For all B knows, C might have ten lines all with separate paths to A of length 2. As a result, B thinks it can reach A via C, with a path length of 3. D and E do not update their entries for A on the first exchange.
On the second exchange, C notices that each of its neighbors claims to have a path to A of length 3. It picks one of the them at random and makes its new distance to A 4, as shown in the third row of Fig. 5-10(b). Subsequent exchanges produce the history shown in the rest of Fig. 5-10(b).
Gradually, all routers work their way up to infinity, but the number of exchanges required depends on the numerical value used for infinity. For this reason, it is wise to set infinity to the longest path plus 1. The core of the problem is that when X tells Y that it has a path somewhere, Y has no way of knowing whether it itself is on the path.

## Slide 31
How do we solve the count-to-infinity problem?

## Slide 32: Split Horizon with Poison Reverse
Split Horizon with Poison Reverse:
Router 1 tells router 2 that the path for X has a metric of infinity.
R1 to X: inf.

## Slide 33: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node's table used by others
    error propagate thru network

## Slide 34
The Internet is huge. Do DV and Link-state work?

## Slide 35: Making routing scalable
scale: with billions of destinations:
can't store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network is flat
But, not true in practice

## Slide 36: Basic idea of scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c

## Slide 37: Overview of hierarchical routing
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
inter-AS routing
intra-AS routing

## Slide 38: Intra-AS vs Inter-AS
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS'es
inter-AS routing
routing among AS'es
gateways perform inter-domain routing (as well as intra-domain routing)

## Slide 39: Job of inter-AS routing
suppose router in AS1 receives datagram destined outside of AS1:
router should forward packet to gateway router, but which one?
job of inter-AS routing!
AS1 should learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
Given x, how to forward?

## Slide 40: Job of intra-AS routing
Job of intra-AS routing: to determine the path entirely within an AS
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 41: How is forwarding table configured?
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests (simple!)
  Both inter-AS & intra-AS set entries for external dests (more complicated, how?)

## Slide 42: Setting forwarding table at a router
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
x
…
Given x, which interface to forward?
suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c) but not via AS2.
inter-AS protocol propagates reachability info to all internal routers.
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c.
  installs forwarding table entry (x,I)

## Slide 43: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 44
A concrete and popular example of intra-AS routing
Open Shortest Path First
OSPF

## Slide 45: Overview of OSPF
open: publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra's algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link
IS-IS routing protocol: nearly identical to OSPF

## Slide 46: OSPF advanced features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 47: Hierarchical OSPF
boundary router to other AS
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 48: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each node has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers:
  summarize distances to nets in own area
  advertise to other Area Border routers.
backbone routers:
  run OSPF routing limited to backbone.

## Slide 49: Routing across areas
1E
3C
How does a packet find the routing path from 1E to 3C?
Routers in area 1, given dest 3C, which next hop?
Routers in backbone, given dest 3C, which next hop?
Routers in area 3, given dest 3C, which next hop?
3A
3B
1A
1B
1C
1D

## Slide 50
A concrete example of inter-AS routing
Border Gateway Protocol
BGP

## Slide 51: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 52: Overview of BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  1: obtain subnet reachability information from neighboring ASes
  2: propagate reachability information to all AS-internal routers.
  3: determine good routes to other networks based on reachability information and policy
BGP allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 53: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
gateway routers run both eBGP and iBGP protocols

## Slide 54: BGP basics
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X
BGP session: two BGP routers exchange BGP messages over TCP connection: advertising paths to different destination network prefixes
  when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c
  AS3 promises to AS2 it will forward datagrams towards X
Notes: Advertisement的内容是什么？给定网络目标地址的可达性信息

## Slide 55
What information should be included in BGP advertisement for a given destination prefix?

## Slide 56: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other neighboring ASes

## Slide 57: BGP path advertisement (One Path Case)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 58: BGP path advertisement (Tow Paths Case)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS1 gateway router 1c learns path AS2,AS3,X from 2a
AS1 gateway router 1c learns path AS3,X from 3a
AS3,X

## Slide 59: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 60: How forwarding table entries are set?
distant prefix X
What is the forwarding entry for X?
It is jointly determined by BGP and OSPF!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X

## Slide 61: Example: forwarding entry at router 1d for X
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
AS3,X
distant prefix X
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1d: OSPF intra-AS routing: to get to 1c, forward over outgoing local interface 1

## Slide 62: Example: forwarding entry at router 1a
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2
distant prefix X

## Slide 63
An internal router may learn about more than one route to destination, then how does it choose?

## Slide 64: Hot Potato Routing
Router 2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don't worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 65: Background for inter-AS routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two network
A
B
C
W
X
Y
legend:
customer
network:
provider
network
How do AS B and C send BGP advertisement?

## Slide 66: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no revenue for routing CBAw, since none of C, A, w are B's customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 67: Why Intra-, Inter-AS routing?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 68: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 69
What are the main problems with Internet’s Control Plane?

## Slide 70: Problems with per-router approach
Internet network layer: historically has been implemented via distributed, per-router approach
The problems with this approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, etc.
~2005: renewed interest in rethinking network control plane
Notes: Monolithic：adj. 整体的；巨石的，庞大的；完全统一的

## Slide 71: Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 72: Recall: logically centralized control plane
data
plane
control
plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 73: Why logically centralized control?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane

## Slide 74: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
* Slide courtesy: N. McKeown

## Slide 75: Traffic engineering: difficult (Case 1)
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route blue and red traffic differently?
A: can't do it (with destination based forwarding, and LS, DV routing)
Notes: Note: implicit assumption here: destination based forwarding

## Slide 76: Traffic engineering: difficult (Case 2)
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can't do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 77
How do you implement software-defined networking?

## Slide 78: Overview of SDN
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance

## Slide 79: Overview of SDN

## Slide 80: SDN perspective: data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
Data plane switches

## Slide 81: SDN perspective: SDN controller
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
SDN controller (or network OS):

## Slide 82: SDN perspective: control applications
“brains” of control: implement control functions using lower-level services, API provided by SND controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
Network-Control Applications

## Slide 83: Components of SDN controller
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer:
state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 84: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
OpenFlow Controller

## Slide 85: Controller-to-switch messages
Key controller-to-switch messages
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
features: controller queries switch features, switch replies
OpenFlow Controller
Fortunately, network operators don't program switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller

## Slide 86: Switch-to-controller messages
Key switch-to-controller messages
flow-removed: flow table entry deleted at switch
packet-in: transfer packet (and its control) to controller.
port status: inform controller of a change on a port.
OpenFlow Controller

## Slide 87: SDN: control/data plane interaction
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra's routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra's routing algorithm access network graph info, link state info in controller, computes new routes
4
Link broken, what happen next?

## Slide 88: SDN: control/data plane interaction
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6

## Slide 89: OpenDaylight (ODL) controller
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services
OpenDaylight（ODL）是Linux基金会负责管理的开源项目，是一款使用JAVA开发的控制器，提供一套基于SDN开发的模块化、可扩展、可升级、支持多协议的控制器框架，目的是推动SDN技术的创新实施和透明化。
Notes: 随着移动设备的不断普及，OTT服务和内容分发的兴起导致服务提供商网络迫切的需要一次网络变革。为了应对日益增长的带宽需求，服务提供商希望网络可以更加敏捷高效，且能从创新型服务和新型业务模式中分一杯羹得到更好的发展，至此SDN的呼声越来越高。而SDN中控制器占重要部分，是兵家必争之地，陆陆续续已经出现了很多SDN控制器，如OpenDaylight、OpenContrail、Ryu、Floodlight、NOX、SPOX等等，其中最受瞩目的莫过于OpenDaylight了。 OpenDaylight是由设备商主导的一个开源控制器，虽然打着开放的旗号，但是OpenDaylight一直排斥基于开放的协议方案，而是想采用折中的方案，即以开放专用接口的方式保留传统设备，采取以退为进的方式维护自己的利益。不可否认地，设备商拥有丰富的设备研发经验， OpenDaylight也确实是一款优秀的控制器，但是在这样的压力下，运营商不得不采取应对措施。于是，运营商推出了开放网络操作系统ONOS。
————————————————
版权声明：本文为CSDN博主「SDNLAB」的原创文章，遵循CC 4.0 BY-SA版权协议，转载请附上原文出处链接及本声明。
原文链接：https://blog.csdn.net/SDNLAB/article/details/41980413

## Slide 90: ONOS controller
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling
Notes: 运营商更关注 ONOS

## Slide 91: Floodlight
Welcome! Floodlight is a community-developed, open source, Java OpenFlow controller, supporting OpenFlow protocols 1.0 through 1.5.
Notes: https://floodlight.atlassian.net/wiki/spaces/floodlightcontroller/overview
https://github.com/noxrepo/pox

## Slide 92: POX SDN Controller

## Slide 93: SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 94: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 95: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 96: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 97: Outline
5.1 introduction
5.2 routing protocols
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP
5.7 Network management and SNMP

## Slide 98: What is network management?
autonomous systems (aka network): 1000s of interacting hardware/software components
other complex systems requiring monitoring, control:
  jet airplane
  nuclear power plant
  others?
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."

## Slide 99: Infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
network
management
protocol
managed device
agent
data
agent
data
agent
data

## Slide 100: SNMP protocol
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response

## Slide 101: SNMP protocol: message types
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: “get me data”
(data instance, next data in list, block of data)
Message type
Function
InformRequest
manager-to-manager: here's MIB value
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to Request
Trap
Agent-to-manager: inform manager
of exceptional event

## Slide 102: SNMP protocol: message formats
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Get/set header
Variables to get/set
Trap header
Trap info
SNMP PDU
More on network management: see earlier editions of text!

## Slide 103: Chapter 5: summary
we've learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS, Floodlight
Internet Control Message Protocol
Network Management
next stop: link layer!

## Slide 104: Lab #4
IP: Wireshark_IP
NAT: Wireshark_NAT
ICMP: Wireshark_ICMP