## Slide 1: Chapter 6: The Link Layer
Yanmin Zhu
School of Computers
Notes: 224.0.0.0〜224.0.0.255:保留地址，用于路由协议或其他下层拓扑发现协议、以及维护管理协议等，例如 224.0.0.1代表本地子网中的所有主机 ，224.0.0.2代表本地子网中的所有路由器， 224.0.0.5代表所有OSPF路由器 ， 224.0.0.9代表所有RIP2路由器 ，224.0.0.12代表DHCP服务器或中继代理，224.0.0.13代表所有支持PIM的路由器等。

## Slide 2: Link-Layer Hops along Host and Server

## Slide 3
Discussions
What are the services provided by the link layer?
How do we characterize the capability of an error detection and correction code?
How does the link layer interplay with the network layer?
How do many nodes access a shared broadcast channel?
Notes: * Application layer, between client/server, assuming TCP/UDP; transport layer, between two processes, assuming network layer services;
These two layers, a communicating party is sure to know the other communicating party (within the known address)
The network layer, between two host, assuming the link layer. It is the job of this layer to find a path from one host to the other host, since the lower layer (i.e., link layer) do not provide such a service. Then, what the service provided by the link layer? Frame delivery between neighboring nodes (host or router) .
What is “neighboring?”
Answer: in a subnet! Link-layer device may be introduced in order to provide such frame delivery service, but these link-layer devices are transparent to the network layer.

## Slide 4: The Data Link Layer
Our goals:
understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
instantiation, implementation of various link layer technologies

## Slide 5: Chapter 6 Link Layer
6.1 Introduction to the link layer
6.2 Error detection and correction
6.3 Multiple access links and protocols
6.4 Switched local area networks
6.5 Link virtualization: A network as a link layer
6.6 Data center networking

## Slide 6
What are the main service provided by the link layer?
data transfer between neighboring network elements

## Slide 7: Link Layer: Teminology
Terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 8: Link Layer: Context
Datagram transferred by different link protocols over different links, e.g.,
  First link: Ethernet
  Intermediate links: frame relay
  Last link: 802.11
Each link protocol provides different services
  e.g., may or may not provide rdt over link

## Slide 9: Link layer services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest: different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates

## Slide 10: Link layer services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 11: Where is link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 12: Adaptors Communicating
sending side:
encapsulates datagram in frame
adds error checking bits, rdt, flow control, etc.
Coding
receiving side：
looks for errors, rdt, flow control, etc
extracts datagram, passes to upper layer at receiving side
decoding
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 13: Link Layer
6.1 Introduction to the link layer
6.2 Error detection and correction
6.3 Multiple access links and protocols
6.4 Switched local area networks
6.5 Link virtualization: A network as a link layer
6.6 Data center networking

## Slide 14: Overview of Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
otherwise
Error detection not 100% reliable!
protocol may miss some errors, but rarely
larger EDC field yields better detection and correction

## Slide 15: Parity Checking
Single Bit Parity:
Detect single bit errors
Example:

## Slide 16: Parity Checking (cont’)
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 17: Cyclic Redundancy Check (CRC)
The cyclic redundancy check (CRC) is a technique used to detect errors in digital data. More powerful error-detection coding
This technique was invented by W. Wesley Peterson in 1961
Cyclic redundancy checks are quite simple to implement in hardware and can be easily analyzed mathematically.
Widely used in practice (Ethernet, 802.11 WiFi, ATM, etc.)

## Slide 18: Representing bit stream as a polynomial
Bit stream:
B=bn-1bn-2…b2b1b0
Polynomial:
B(x)=bn-1xn-1 + bn-2xn-2 + … + b2x2 + b1x1 + b0
Example
Preliminary

## Slide 19: Computing Remainder
Computing remainder
Computing remainder
Example
It is based on binary division!

## Slide 20: CRC overview
Receiver
Sender

## Slide 21: How to compute R(x)?
R = remainder[ ]
Dx2r
G

## Slide 22: CRC Example
D: 101110
G: 1001
R(x): 011
Data plus redundancy to send
101110011

## Slide 23: Popular CRC Protocols

## Slide 24: Error Detection Performance of CRC
A CRC-n code can detect any error pattern that affects an odd number of bits.
It can detect all burst errors of length ( n ) or less.
It can detect most larger errors, although the probability of undetected errors increases as the error pattern length exceeds ( n ).

## Slide 25
How do you characterize the performance of a code for error detection and correction?
2-bit data:
01
Even parity coding
011
3-repetition coding
000111

## Slide 26: Hamming Distance
Definition: hamming distance (HD) is the number of positions at which the corresponding symbols are different
000
011
001
111
Hamming distance = 3
00
01
10
11
Valid codeword
Invalid codeword
101
010
110
100
Valid codeword
Hamming distance = 2
Invalid codeword
Code 1
Code 2

## Slide 27: Minimum Hamming distance required

## Slide 28: Characterizing Performance of a Code

## Slide 29: Link Layer
6.1 Introduction to the link layer
6.2 Error detection and correction
6.3 Multiple access links and protocols
6.4 Switched local area networks
6.5 Link virtualization: A network as a link layer
6.6 Data center networking

## Slide 30: Multiple Access Links and Protocols
Two types of “links”:
Type 1: point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch and host
Type 2: broadcast (shared wire or medium)
  old-fashioned Ethernet
  Upstream TV Cable
  802.11 wireless LAN
humans at a
cocktail party
(shared air, acoustical)

## Slide 31: Multiple access to a shared link
Shared link
Link capacity = R pbs
Node 1
Node 2
Node 3
Node N

## Slide 32: Multiple Access Protocols
Model:
  (1) single shared broadcast channel
  (2) two or more simultaneous transmissions by nodes: interference
    collision if node receives two or more signals at the same time
multiple access protocol (MAC)
An algorithm that determines how nodes share channel, i.e., determine when node can transmit
Assumption: communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 33
What is an ideal MAC protocol?

## Slide 34: Ideal Multiple Access Protocol
1. when one node wants to transmit, it can send at rate R.
2. when M nodes want to transmit, each can send at average rate R/M
3. fully decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks, slots
4. simple

## Slide 35: MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  nodes take turns
  nodes with more to send can take longer turns
static
dynamic

## Slide 36: Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame

## Slide 37: Channel Partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 38: Frequency Division Multiplexing
(a) The original bandwidths.
(b) The bandwidths raised in frequency.
(c) The multiplexed channel.

## Slide 39: Wavelength Division Multiplexing

## Slide 40
What are drawbacks of static channel-partitioning protocols?

## Slide 41
How do you overcome the drawbacks?

## Slide 42: Basic idea
Shared link
Link capacity = R pbs
Node 1
Node 2
Node 3
Node N
When a node accesses the link, it uses the whole capacity of the link!
The key is to avoid collisions (i.e., nodes transmit at the same time)

## Slide 43: Random Access Protocols
Random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  ALOHA
  slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 44: Pure (unslotted) ALOHA
when frame first arrives, a node transmits immediately
If collision, immediately retransmits with probability p and waits for a frame time with probability 1-p;
Feature: simple, no synchronization
Protocol operations

## Slide 45: Pure Aloha efficiency
P(success by given node)
= P(node transmits) . P(no other node transmits in [t0-1,t0] . P(no other node transmits in [t0,t0+1]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
choosing optimum p and then letting N -> inf...
= 1/(2e) = 0.18
Efficiency : long-run fraction of successful slots (many nodes, all with many frames to send)
collision happens when:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 46: Slotted ALOHA
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
Protocol operations

## Slide 47: Slotted Aloha efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
Given a node, prob that has success in a slot
= p(1-p)N-1
prob that any node has a success
= Np(1-p)N-1
Max efficiency = 1/e = 0.37

## Slide 48: Throughput Comparison
Throughput versus offered traffic for ALOHA systems
Notes: The relation between the offered traffic and the throughput is shown in Fig. 4-3. The maximum throughput occurs at G = 0.5, with S = 1/2e, which is about 0.184. In other words, the best we can hope for is a channel utilization of 18 percent. This result is not very encouraging, but with everyone transmitting at will, we could hardly have expected a 100 percent success rate.
e = 2.7182818284590

## Slide 49
What is the main reason for Aloha’s low efficiency?
Transmissions without considering
transmissions of other nodes!

## Slide 50: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
human analogy: don’t interrupt others!
(1) the adapter senses the channel
if idle, it starts to transmit the frame immediately
if not, it waits until it senses a clear channel and transmits the frame
Protocol operations

## Slide 51: CSMA collisions
collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission
collision:
entire packet transmission
time wasted
spatial layout of nodes
note:
role of distance & propagation delay in determining collision probability

## Slide 52: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collision detection: measure signal strengths, compare transmitted, received signals
  colliding transmissions aborted, reducing channel wastage
(1) the adapter senses the channel
if idle, it starts to transmit the frame immediately
if not, it waits until it senses a clear channel and transmits the frame
(2) while transmitting, the adapter monitors for collisions
if collision, abort immediately
if not, transmission is successful
(3）after aborting, it waits for a random amount of time (exponential backoff)
Protocol operations

## Slide 53: CSMA/CD collision detection

## Slide 54
Except static partitioning protocols, can any MAC protocol avoid packet collisions?

## Slide 55: “Taking Turns” MAC protocols
(1) channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
(2) random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
(3) “taking turns” protocols
  look for best of both worlds!

## Slide 56: “Taking Turns” MAC protocols
Basic idea of polling
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
master
slaves
poll
data
data
Concerns:
  polling overhead
  latency
  single point of failure (master)

## Slide 57: “Taking Turns” MAC protocols
Basic idea of Token passing:
control token passed from one node to next sequentially.
token message
T
data
(nothing
to send)
T
Concerns:
  token overhead
  latency
  single point of failure (token)

## Slide 58: Summary of MAC protocols
(1) channel partitioning, by time, frequency or code
  Time Division, Frequency Division
(2) random access
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  Collision detection: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
(3) taking turns
  polling from central site, token passing
  Bluetooth, FDDI, IBM Token Ring

## Slide 59: Cable access network
cable headend
CMTS
ISP
cable modem
termination system
Downstream: multiple 40Mbps downstream (broadcast) channels
  single CMTS transmits into channels （no contention!）
Upstream: multiple 30 Mbps upstream channels
  multiple access （contention!）: all users contend for certain upstream channel time slots (others assigned)
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
upstream Internet frames, TV control, transmitted
upstream at different frequencies in time slots

## Slide 60: Cable access network (cont’)
DOCSIS: data over cable service interface spec
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
MAP frame for
Interval [t1, t2]
Residences with cable modems
Downstream channel i
Upstream channel j
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS

## Slide 61: Link Layer
6.1 Introduction to the link layer
6.2 Error detection and correction
6.3 Multiple access links and protocols
6.4 Switched local area networks
6.5 Link virtualization: A network as a link layer
6.6 Data center networking

## Slide 62: Switched Local area networks
Router
switch
switch
switch
switch

## Slide 63: 6.4 Switched local area networks
1. Link-layer addressing and ARP
2. Ethernet
3. Link-layer switches
4. Virtual local area networks (VLANs)

## Slide 64: MAC Addresses
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs)
    burned in NIC ROM, also sometimes software settable
Permanent, globally unique

## Slide 65: LAN Addresses
Each adapter on LAN has unique LAN address
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 66: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  address depends on IP subnet to which node is attached
analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address

## Slide 67
Why both MAC and IP address?

## Slide 68: Why both MAC and IP address?
(1) The data link layer does not only serve IP protocol, including many others
(2) if adapters use network-layer address, then the adapter needs to be reconfigured every time it moves
(3) if not use MAC add at all, then all received frames should be forwarded to network layer. Great overhead!
Answer: to keep the layers independent

## Slide 69
How do MAC address and IP address interact?

## Slide 70: MAC Address interacting with IP
Question: When sending a packet to B, how does A gets B’s MAC address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
A
B
Note: The sender, A, gets B’s IP via DNS, but does not have B’s MAC!

## Slide 71: ARP: Address Resolution Protocol
Each IP node (host, router) on LAN has ARP table
ARP table: IP/MAC address mappings for some LAN nodes < IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
ARP: Mapping IP address to MAC address

## Slide 72: ARP protocol: Same LAN (network)
A wants to send datagram to B, and B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  dest MAC address = FF-FF-FF-FF-FF-FF
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 73: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 74: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 75: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 76: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 77: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 78: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy

## Slide 79: 6.4 Switched local area networks
1. Link-layer addressing and ARP
2. Ethernet
3. Link-layer switches
4. Virtual local area networks (VLANs)

## Slide 80: Ethernet
“dominant” wired LAN technology:
cheap $20 for NIC
first widely used LAN technology
simpler, cheaper than token LANs and ATM
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet
sketch

## Slide 81: Bus Topology
Old fashioned, Based on Coax (Ethernet 10base2)
Bus topology popular through mid 90s

## Slide 82: Star topology
today: star topology prevails
active switch in center
each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
star

## Slide 83: Ethernet Services
connectionless:
  No handshaking between sending and receiving NICs
unreliable:
  receiving NIC doesn’t send acks or nacks to sending NIC
  stream of datagrams passed to network layer can have gaps (missing datagrams)
  gaps will be filled if app is using TCP
  otherwise, app will see gaps

## Slide 84: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates

## Slide 85: Ethernet Frame Structure (more)
Addresses: 6 bytes
  if adapter receives frame with matching destination address, or with broadcast address (eg ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
Type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: checked at receiver, if error is detected, frame is dropped
multiplexing

## Slide 86: Ethernet MAC: CSMA/CD
Step 1. NIC receives datagram from network layer, creates frame
Step 2. Carrier sensing
  If NIC senses channel idle, starts frame transmission
  If NIC senses channel busy, waits until channel idle, then transmits
Step 3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
Step 4. If NIC detects another transmission while transmitting, aborts and sends jam signal

## Slide 87: Exponential Backoff
After aborting, NIC enters exponential backoff: after mth collision, NIC chooses K at random from {0,1,2,…,2m-1}.
NIC waits K·512 bit times, returns to Step 2

## Slide 88: Why Exponential?
When there are a small number of competitors, resolve completion in short time => wait a short time
When there are a larger number of competitors, resolve completion in longer time
When experiencing more collisions, be aware of more competitors
Goal of exponential backoff:
adapt retransmission attempts to estimated current load

## Slide 89: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits
Bit time: 0.1 microsec for 10 Mbps Ethernet ; for K=1023, wait time is about 50 msec
Exponential Backoff example:
first collision: choose K from {0,1}; delay is K· 512 bit transmission times
after second collision: choose K from {0,1,2,3}…
after ten collisions, choose K from {0,1,2,3,4,…,1023}
See/interact with Java
applet on AWL Web site:
highly recommended !
demo

## Slide 90: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 91: 6.4 Switched local area networks
1. Link-layer addressing and ARP
2. Ethernet
3. Link-layer switches
4. Virtual local area networks (VLANs)

## Slide 92
How do we physically connect devices in the same subnet?

## Slide 93: Hubs
physical-layer (“dumb”) repeaters:
  bits coming in one link go out all other links at same rate
  all nodes connected to hub can collide with one another
  no frame buffering
  no CSMA/CD at hub: host NICs detect collisions
Hub
Collision domain

## Slide 94: Switch
Switch
link-layer device: smarter than hubs, take active role
  store, forward Ethernet frames
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured
Collision domain
Collision domain

## Slide 95: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
  not possible with dumb hub
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 96: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 97: Switch: self-learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 98: Switch: frame filtering/forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 99: Self-learning, forwarding: example
frame destination unknown:
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
flood
A’ A
destination A location known:
A’
4
60
selective send

## Slide 100: Interconnecting switches
switches can be connected together
A
B
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 101: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
1
2

## Slide 102: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 103: Switches vs. Routers
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms

## Slide 104: Switches vs. Routers (2)
Switch |  | Router | 
Pro | Con | Pro | Con
Plug-and-play | Broadcast storms Topology restricted to spanning tree | No broadcast storms More general topologies | Not plug-and-play

## Slide 105: 6.4 Switched local area networks
1. Link-layer addressing and ARP
2. Ethernet
3. Link-layer switches
4. Virtual local area networks (VLANs)

## Slide 106: VLANs: motivation
What are the problems with a hierarchical LAN connecting different groups?
Lack of traffic isolation among groups
Security/privacy risk
Management of user movement among groups
Group 1
Router
switch
switch
switch
switch
Group 2
Group 3

## Slide 107: Basic idea of VLAN
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local Area Network
Router
VLAN1
VLAN2
VLAN3
Group 1
Group 2
Group 3

## Slide 108: Port-based VLAN
switch ports grouped (by switch management software) so that single physical switch ……
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
operates as multiple virtual switches

## Slide 109: Port-based VLAN
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 110: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches cannot be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 111: 802.1Q VLAN frame format
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 112: Real Case Study: New North Campus of the University

## Slide 113: Real Case Study: New North Campus of the University

## Slide 114: Real Case Study: New North Campus of the University

## Slide 115: Real Case Study: New North Campus of the University

## Slide 116: CloudEngine S6735-S系列交换机

## Slide 117: Link Layer
6.1 Introduction to the link layer
6.2 Error detection and correction
6.3 Multiple access links and protocols
6.4 Switched local area networks
6.5 Link virtualization: A network as a link layer
6.6 Data center networking

## Slide 118: Overview of MPLS
Multiprotocol label switching (MPLS)
MPLS is a packet-switched, virtual-circuit network in its own right
Pedagogical viewpoint
The network layer
The link layer
The Internet viewpoint
A link-layer technology for interconnecting two IP devices

## Slide 119: MPLS Example
R1
R2
R3
R4
R5
0
1
0
0
A
R6
1
0
MPLS network
R8
R7
A virtual-circuit network

## Slide 120: Multiprotocol label switching (MPLS)
initial goal: high-speed IP forwarding using fixed length label (instead of IP address)
  fast lookup using fixed length identifier (rather than shortest prefix matching)
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
Transport header
MPLS header
label
Exp
S
TTL
20
3
1
5

## Slide 121: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1
App
Transport
Network
MPLS
Link
Physical
App
Transport
Network
MPLS
Link
Physical
label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
MPLS forwarding table distinct from IP forwarding tables

## Slide 122: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
D
R4
R5
A
R6
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
modified
link state
flooding
RSVP-TE

## Slide 123: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4
flexibility: MPLS forwarding decisions can differ from those of IP： use destination and source addresses to route flows to same destination differently (traffic engineering)

## Slide 124: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and dest. address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address

## Slide 125: Link Layer
6.1 Introduction to the link layer
6.2 Error detection and correction
6.3 Multiple access links and protocols
6.4 Switched local area networks
6.5 Link virtualization: A network as a link layer
6.6 Data center networking

## Slide 126: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 127: Typical Architecture
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Border router
Access router
Internet
Access router
Two types of traffic

## Slide 128
What are the design objectives of a data center network?

## Slide 129: Rich interconnection among switches
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
increased throughput between racks (multiple routing paths possible)
increased reliability via redundancy

## Slide 130: Putting all together:

## Slide 131: Network Setting
A student, Bob, connects a laptop to his school’s Ethernet switch
He downloads a Web page (say the home page of www.google.com)

## Slide 132: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS

## Slide 133: Let’s take a breath
journey down protocol stack complete (including except including PHY communications)
solid understanding of networking principles, practice

## Slide 134: Homework #05: Chapter 6: P5, P10, P13, P21