## Slide 1: Chapter 7: Wireless and Mobile Networks
Yanmin Zhu
School of Computers

## Slide 2
Already finished all layers in the stack, why a separate chapter for wireless and mobile networks?
Key differences: Wireless and mobile

## Slide 3
Considering wireless characteristics, what shall be different on link layer, network layer, transport layer and application layer?

## Slide 4
Considering mobility, what shall be different on link layer, network layer, transport layer and application layer?

## Slide 5: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 6: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 7: Elements of a wireless network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility

## Slide 8: Elements of a wireless network
network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 9: Elements of a wireless network
network
infrastructure
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance

## Slide 10: Characteristics of wireless standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac
5G

## Slide 11: Modes of wireless network
network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 12: Modes of wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 13: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 14: Mesh Networks

## Slide 15: Vehicular Ad Hoc Networks (VANETs)
V2V
V2I
I2V

## Slide 16: Why VANET?

## Slide 17: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 18
What are the main characteristics of wireless links, compared with wired links?

## Slide 19: Wireless Link Characteristics (1)
Differences from wired link
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
Thus, these differences make communication across (even a point to point) wireless link much more “difficult”

## Slide 20: Wireless Link Characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest thruput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 21: FDMA, TDMA, CDMA

## Slide 22: Basic Idea of CDMA
unique “code” assigned to each user; i.e., code set partitioning
all users share same frequency, but each user uses own code to encode data
A receiver uses the sender’s code to recover the sent bits
Code Division Multiple Access (CDMA)
  encoded signal = (original data) X (chipping sequence)
  decoding: inner-product of encoded signal and chipping sequence

## Slide 23: CDMA Encode/Decode: One Sender
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 24: CDMA Encode/Decode: Tow Senders
A
1
0
1
1
0
1
B
Code of A
Reception from A

## Slide 25: CDMA
A
B
C
D
E
SCENARIO 1
SCENARIO 2
SCENARIO 3
What C transmits?

## Slide 26: Codes

## Slide 27
Who is the inventor of CDMA?

## Slide 28: A note on Inventor
Hedy Lamarr
1914/11/9—2000/1/19
1941, Original for Torpedo
1985 QUALCOMM

## Slide 29: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 30: WLAN architecture
Wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router
AP
AP

## Slide 31: 802.11b Channels
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
Question: what is the maximum throughput if you deploy multiple WiFi APs in a room?

## Slide 32: Association before Transmission
Host: must associate with an AP
scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
selects AP to associate with
may perform authentication
will typically run DHCP to get IP address in AP’s subnet

## Slide 33: Two types: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
Active Scanning:
Probe Request frame broadcast from H1
Probes response frame sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent: H1 to selected AP
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
Passive Scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent: H1 to selected AP

## Slide 34: Multiple Access for Wireless Channel
CSMA may fail!
Why?
AP
H1
H2
H3

## Slide 35: Due to Hidden Terminal Problem!
A
B
C
Comm. Range
Collision happen at B
A->B
C->B
A transmits
C transmits
time
time
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 36: Multiple access control protocol
avoid collisions: 2+ nodes transmitting at same time
CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
AP
H1
BSS
H2
H3

## Slide 37: CSMA for 802.11
DIFS
data
SIFS
ACK
Sense the channel
  If idle for DIFS, transmit entire frame (no CD), wait for ACK
  If busy - select random backoff interval - timer counts down while channel idle - transmit when timer expires
Wait for ACK
  If ACK received, done
  If no ACK, double contention window and re-select random backoff interval, repeat
sender
receiver
Protocol operations

## Slide 38
Why two different space intervals (i.e., DIFS and SIFS)?

## Slide 39: WiFi CSMA vs Ethernet
What are the key differences?
(1) WiFi has ACK, since radio links are more error prone
(2) WiFi starts random backoff as soon as it senses a busy channel, why?
But no collision detection, why?
Difficult to receive while transmitting
Anyway, cannot detect all collisions, due to hidden terminal problem
No collision detection, so more conservative!

## Slide 40: Idea of Avoiding Collisions
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send (CTS) in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames

## Slide 41: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 42
A few important design details:
When to decrement the counter, before or after DIFS?
When to freeze the backoff timer?

## Slide 43: Timing of the 802.11
In this example, station 6 cannot detect the RTS frame of the transmitting station 2, but the CTS frame of station 1.

## Slide 44: Two Animations
DEMO1
DEMO2

## Slide 45: Three Modes of Service Sets
Mode 1:
Independent Basic Service Set (IBSS)
H1
H2
H3
Independent Basic Service Set (IBSS) allows two or more devices to communicate directly with each other without a need for a central device

## Slide 46: Three Modes of Service Sets
Mode 2:
Basic Service Set (BSS)
All mobile devices do not communicate directly, instead through the access point (AP).
AP
H1
BSS
H2
H3

## Slide 47: Three Modes of Service Sets
Mode 3:
Extended Service Set (ESS)
ESS is created by connecting multiple Basic Service Set (BSS) via a distribution system
AP
H1
BSS1
H2
H3
AP
H5
BSS2
H4
SSID: sameid
SSID: sameid
switch

## Slide 48: 802.11: mobility within same subnet
H1 remains in same IP subnet:
  IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1
switch
AP 2
AP 1
H1
BBS 2
BBS 1
router
Good, but what about switching?

## Slide 49: Sending Frames between H1 & A Remote Host
Note:
Two link-layer technologies
Remote Host
Can we use Ethernet frame format for WLAN?
R1 not aware of existence of AP
Notes: Switch vs AP, switch 没有MAC地址，而AP是有MAC地址的。

## Slide 50: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 51: 802.11 frame: addressing
Internet
router
AP
H1
R1
H1 MAC addr AP MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
H1 MAC addr R1 MAC addr
dest. address
source address
802.3 frame
Frame conversion
Remote Host
R1 not aware of existence of AP

## Slide 52: 802.11 frame: addressing
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
Frame conversion
Remote Host

## Slide 53
What information should be included in 802.11b frame header?

## Slide 54: 802.11 frame: more
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT)
frame type
(RTS, CTS, ACK, data)
Byte
Bit

## Slide 55: 802.11: advanced capabilities
Rate Adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 56: 802.11: advanced capabilities
Power Management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent;
  otherwise sleep again until next beacon frame

## Slide 57: 802.11: advanced capabilities
The beacon frame contains the list of hosts with pending frames to receive
beacon
beacon
beacon
beacon
A
B
A
A, B

## Slide 58: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
    all hosts use same chipping code
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
  WIFI 5
802.11ax
  2.4-5 GHz range
  Up to 600 Mbps
  WIFI 6
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 59: Wi-Fi Standards

## Slide 60: Brief Introduction to OFDM
FDM
OFDM
Physical Layer, to improve efficiency and robustness. Not Link layer tech. MAC still needed!
Notes: OFDM 主要解决的是物理层的问题，通过频分复用来提高传输效率和抗干扰能力。

## Slide 61: OFDM Signal Frequency Spectra

## Slide 62: Basic Idea
sin(t)和sin(2t)是正交的，因为sin(t)·sin(2t)在区间[0,2π]上的积分为0
Carrier 1: sin(t)
Carrier 2: sin(2t)

## Slide 63: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 64: From 1G to 5G

## Slide 65: Development of cellular technology
Notes: IMT 和 3GPP Release 版本的对应关系
IMT-2000
  3GPP Release 99 到 Release 5
    技术: WCDMA、HSPA（从 Release 5 开始引入 HSDPA）
    特点: 这是第三代移动通信技术，支持语音、文本和基础数据服务。
IMT-Advanced
  3GPP Release 8 和 Release 10
    Release 8: 引入 LTE（Long Term Evolution）
    Release 10: 引入 LTE-Advanced
    特点: 这是第四代移动通信技术，提供更高的数据速率和更低的延迟。
IMT-2020
  3GPP Release 15 和之后的版本
    Release 15: 首个 5G NR 标准
    Release 16: 进一步完善 5G，包括增强的 URLLC 和 mMTC
    特点: 第五代移动通信技术，支持超高速数据传输、超低延迟、大规模设备连接。
关键点
Release 演进: 每个 Release 版本引入新的特性和改进，支持更高效的通信技术。
标准提交: 3GPP 的 Release 版本经过验证后，提交给 ITU 作为 IMT 标准的一部分。
全球一致性: 确保全球网络的互操作性和一致性，促进全球移动通信的发展。
这种对应关系确保了移动通信技术的全球统一性和持续演进。
ITU（国际电信联盟）和 3GPP（第三代合作伙伴计划）之间有着密切的合作关系，但它们的角色和职责有所不同。
ITU（国际电信联盟）
职责: ITU 是联合国的一个专门机构，负责全球电信和无线电频谱的协调和标准化。它制定全球通信标准，管理频谱分配，确保不同国家和地区的技术兼容性。
作用: 提供一个全球框架，确保各国在频谱使用和技术标准上协调一致。
3GPP（第三代合作伙伴计划）
职责: 3GPP 是一个行业组织，专注于移动通信技术标准的制定，如 GSM、UMTS、LTE 和 5G NR。它由多个标准制定机构组成，负责具体技术细节的开发和标准化。
作用: 制定具体的技术标准和规范，推动全球移动通信技术的发展。
关系
合作: 3GPP 制定的技术标准通常会提交给 ITU，后者将这些标准纳入其全球框架中。例如，3GPP 的 LTE 和 5G NR 标准被 ITU 采纳为 IMT（国际移动通信）标准的一部分。
互补性: ITU 提供宏观的政策和频谱管理框架，而 3GPP 负责具体技术的开发和细化，两者共同推动全球移动通信的协调发展。
3GPP2 没有与 3GPP 合并，而是逐渐淡出了主流移动通信标准的制定。3GPP2 主要负责开发 CDMA2000 系列标准，这些标准在北美和部分亚洲市场曾被广泛使用。然而，随着全球移动通信技术向 LTE 和 5G 发展的趋势，3GPP 的标准（如 LTE 和 5G NR）获得了更广泛的采用和支持。
因此，3GPP2 的影响力和市场份额逐渐减少，行业重心转向了 3GPP 制定的标准。许多运营商已经从 CDMA2000 网络迁移到 LTE 和 5G 网络，这也是 3GPP2 标准逐步淡出的原因之一。

## Slide 66: Components of cellular network
Mobile
Switching
Center
Public telephone
network
Mobile
Switching
Center
connects cells to wired tel. net.
manages call setup (more later!)
handles mobility (more later!)
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 67: Cellular networks: the first hop
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency
bands
time slots

## Slide 68: 2G (voice) network architecture
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
MSC
Public
telephone
network
Gateway
MSC
G

## Slide 69: 3G (voice+data) network architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 70: 3G (voice+data) network architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
GGSN
G
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
core network
General Packet Radio Service
(GPRS) Core Network
public
Internet
radio interface
(WCDMA, HSPA)

## Slide 71: 4G: differences from 3G
all IP core: IP packets tunneled (through core IP network) from base station to gateway
no separation between voice and data – all traffic carried over IP core to gateway
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
Public
Internet
P-GW
G
S-GW
G
UE
(user element)
eNodeB
(base station)
Packet data
network
Gateway
(P-GW)
Serving
Gateway
(S-GW)
data
MME
HSS
Mobility
Management
Entity (MME)
control
Home Subscriber
Server(HSS)
(like HLR+VLR)

## Slide 72: 3G versus 4G LTE network architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
G
GGSN
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
MME
Public
Internet
P-GW
G
S-GW
G
HSS
3G
4G-LTE

## Slide 73: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 74: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access points while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.
Notes: Mobility 高还是低，跟要求（demand）有关系！

## Slide 75
How do we support mobile Internet access?

## Slide 76: Mobility: Vocabulary
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
Permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote
wide area network
correspondent

## Slide 77: Mobility: more vocabulary
Care-of-address: address in visited network.
(e.g., 79.129.13.2)
wide area network
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
Permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 78: How do you contact a mobile friend?
search all phone books?
call her parents?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing addresses, how do you find her?

## Slide 79: Mobility: approaches (1)
routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
routing tables indicate where each mobile located
no changes to end-systems
not
scalable
to millions of
mobiles
Let routing handle it (the network core approach):

## Slide 80: Mobility: approaches (2)
indirect routing:
  communication from correspondent to mobile goes through home agent, then forwarded to remote
direct routing:
  correspondent gets foreign address of mobile, sends directly to mobile
let end-systems handle it:

## Slide 81: Mobility: registration
Eventually:
Foreign agent knows about mobile
Home agent knows location of mobile
wide area network
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 82: Mobility via Indirect Routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 83: Indirect Routing
Mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
foreign agent functions may be done by mobile itself

## Slide 84: Can a mobile move to another network?
suppose mobile user moves to another network
  1) registers with new foreign agent
  2) new foreign agent registers with home agent
  3) home agent update care-of-address for mobile
  4) packets continue to be forwarded to mobile (but with new care-of-address)
mobility, changing foreign networks transparent: ongoing connections can be maintained!

## Slide 85: Indirect routing, any problem?
triangle routing problem: correspondent-home-network-mobile
  inefficient when correspondent, mobile are in same network

## Slide 86: Mobility via Direct Routing
wide area network
home
network
visited
network
4
2
4
1
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent
3

## Slide 87: Mobility via Direct Routing: comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?

## Slide 88: Any new problem arise?
new foreign
agent
new
foreign
network

## Slide 89: Accommodating mobility with direct routing
wide area network
1
foreign net visited
at session start
anchor
foreign
agent
2
4
new foreign
agent
3
5
correspondent
agent
correspondent
new
foreign
network
anchor foreign agent: FA in first visited network
data always routed first to anchor FA
when mobile moves: new FA arranges to have data forwarded from old FA
Correspondent just has the IP address at the beginning (1st take-care-off add)

## Slide 90: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 91: Mobile IP
RFC 3344
has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
three components to standard:
  indirect routing of datagrams
  agent discovery
  registration with home agent

## Slide 92: Mobile IP: indirect routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
dest: 79.129.13.2
dest: 128.119.40.186
packet sent by home agent to foreign agent: a packet within a packet
dest: 128.119.40.186
foreign-agent-to-mobile packet

## Slide 93: Mobile IP: agent discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
R bit: registration required
H,F bits: home and/or foreign agent

## Slide 94: Mobile IP: registration example

## Slide 95: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 96: Components of cellular network
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers
recall:

## Slide 97: Handling mobility in cellular networks
home network: network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  home location register (HLR): database in home network containing
    permanent cell phone #,
    profile information (services, preferences, billing),
    information about current location (could be in another network)
visited network: network in which mobile currently resides
  visitor location register (VLR): database with entry for each user currently in network
  could be home network

## Slide 98: GSM: indirect routing to mobile
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile

## Slide 99: GSM: handoff with common MSC
Handoff goal: route call via new base station (without interruption)
reasons for handoff:
  stronger signal to/from new BSS (continuing connectivity, less battery drain)
  load balance: free up channel in current BSS
  GSM doesn’t mandate why to perform handoff (policy), only how (mechanism)
handoff initiated by old BSS
Mobile
Switching
Center
VLR
old BSS
new BSS
old
routing
new
routing

## Slide 100: GSM: handoff with common MSC
1. old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
7. mobile, new BSS signal to activate new channel
8. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
9. MSC-old-BSS resources released
Mobile
Switching
Center
VLR
old BSS
1
3
2
4
5
6
7
8
new BSS

## Slide 101: GSM: handoff between MSCs
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
IS-41 allows optional path minimization step to shorten multi-MSC chain
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(a) before handoff

## Slide 102: GSM: handoff between MSCs
anchor MSC: first MSC visited during call
  call remains routed through anchor MSC
new MSCs add on to end of MSC chain as mobile moves to new MSC
IS-41 allows optional path minimization step to shorten multi-MSC chain
home network
Home MSC
PSTN
correspondent
MSC
anchor MSC
MSC
MSC
(b) after handoff

## Slide 103: Mobility: GSM versus Mobile IP
GSM element |  | Comment on GSM element | Mobile IP element | 
Home system | Network to which mobile user’s permanent phone number belongs |  |  | Home network
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR) | Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information |  |  | Home agent
Visited System | Network other than home system where mobile user is currently residing |  |  | Visited network
Visited Mobile services Switching Center. Visitor Location Record (VLR) | Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user |  |  | Foreign agent
Mobile Station Roaming Number (MSRN), or “roaming number” | Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent. |  |  | Care-of-address

## Slide 104: Chapter 7 outline
7.1 Introduction
7.2 Wireless links and network characteristics
7.3 WiFi: 802.11 wireless LANs
7.4 Cellular Internet access
7.5 Mobility management: principles
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Impact on higher-layer protocols

## Slide 105
What is the impact of wireless links and mobility on high layer protocols?

## Slide 106: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 107: Chapter 7 summary
Wireless
wireless links:
  capacity, distance
  channel impairments
  CDMA
IEEE 802.11 (“Wi-Fi”)
  CSMA/CA reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., GSM, 3G, 4G LTE)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP
  mobility in GSM
impact on higher-layer protocols